## Slide 1: MODULE:2 Environmental quality
SUBJECT: Environmental protection and management
SUBJECT CODE: 18CV753
DEPT. OF CIVIL ENGG.
K.S. SCHOOL OF ENGG. & MANAGEMENT
NAME OF THE FACULTY: Dr Rashmi H R,
Asst. Prof.

## Slide 2: Module 2
Environmental quality objectives – Rationale of Environmental standards: Concentration and Mass standards, Effluent and stream standards, Emission and ambient standards, Minimum national standards, environmental performance evaluation: Indicators, benchmarking. Pollution control Vs Pollution Prevention - Opportunities and Barriers – Cleaner production and Clean technology, closing the loops, zero discharge technologies -8 Hours

## Slide 3: ENVIRONMENTAL MANAGEMENT
Environmental management and its strategy -
Characterized by long-term objectives and
Business areas
(Company wants to be active and tries to obtain
the necessary resources in order to succeed in
the competitive environment)

## Slide 4
Environmental strategy means
Compliance with the obligations set by the applicable legislation and
Voluntary decision of the company to mitigate its impact on the environment.

## Slide 5: aim of environmental management
To minimize the damage caused to the environment
To reduce the amount of waste
An efficient use of natural resources
Protection of biodiversity
Climate and others

## Slide 6: In the longer run
Companies may profit from a range of other benefits
Improvement of the financial results
Enhancing company reputation
Recruiting new and retaining the existing employees
(- To build a strong position of the enterprise on the market
- To acquire new business opportunities
-To reduce costs in the individual areas of its business activities)

## Slide 7: Environmental Quality Objectives
Reduced Climate Impact
Clean Air
Natural Acidification only
A Non-Toxic Environment
A Protective Ozone Layer
A Safe Radiation Environment
Zero Eutrophication
Flourishing Lakes and Streams

## Slide 8: Objectives cont….
Good-Quality Groundwater
A Balanced Marine Environment, Flourishing Coastal Areas
Thriving Wetlands
Sustainable Forests
A Varied Agricultural Landscape
A Magnificent Mountain Landscape
A Good Built Environment
A Rich Diversity of Plant and Animal Life

## Slide 9: 1. Reduced Climate Impact
The UN Framework Convention on Climate Change - stabilization of concentrations of greenhouse gases in the atmosphere at level - ensure that human activities do not have a harmful impact on the climate system
Goal achieved - biological diversity is preserved, food production is assured and other goals of sustainable development
All countries, must have responsibility for achieving global objective

## Slide 10: 2. Clean Air
The air must be clean enough not to represent a risk to health or to animals, plants or cultural assets

## Slide 11: 3. Natural Acidification Only
Acidifying effects of deposition and land use must not exceed the limits that can be tolerated by soil and water.
Deposition of acidifying substances must not increase the rate of corrosion of materials or cultural artefacts and buildings

## Slide 12: 4. A Non-Toxic Environment
The environment must be free from man-made or extracted compounds and metals that represent a threat to human health or biological diversity

## Slide 13: 5. A Protective Ozone Layer
The ozone layer must be replenished so as to provide long-term protection against harmful UV radiation

## Slide 14: 6. A Safe Radiation Environment
Human health and biological diversity must be protected against the harmful effects of radiation in the external environment

## Slide 15: 7. Zero Eutrophication
Nutrient levels in soil and water
Adversely affect human health
Biological diversity
Possibility of varied use of land and water use

## Slide 16: 8. Flourishing Lakes and Streams
Lakes and watercourses must be ecologically sustainable and its variety of habitats must be preserved
Natural productive capacity, biological diversity, cultural heritage assets and the ecological and water-conserving function of the landscape must be preserved, at the same time as recreational assets are safeguarded

## Slide 17: 9. Good-Quality Groundwater
Groundwater must provide a safe and sustainable supply of drinking water

## Slide 18: 10. A Balanced Marine Environment and Flourishing Coastal Areas
The sustainable productive capacity, and biological diversity must be preserved
Coasts must be characterized by a high degree of biological diversity and a wealth of recreational, natural and cultural assets
Industry, recreation and other utilization of the seas, coasts must be compatible with the promotion of sustainable development
Particularly valuable areas must be protected against encroachment and other disturbance

## Slide 19: 11. Thriving Wetlands
The ecological and water-conserving function of wetlands in the landscape must be maintained and valuable wetlands preserved for the future

## Slide 20: 12. Sustainable Forests
The value of forests and forest land for biological production must be protected, at the same time as biological diversity and cultural heritage and recreational assets are safeguarded

## Slide 21: 13. A Varied Agricultural Landscape
The value of the farmed landscape and agricultural land for biological production and food production must be protected, at the same time as biological diversity and cultural heritage assets are preserved and strengthened

## Slide 22: 14. A Magnificent Mountain Landscape
The pristine character of the mountain environment must be largely preserved, in terms of biological diversity, recreational value, and natural and cultural assets
Activities in mountain areas must respect these values and assets, with a view to promoting sustainable development
Particularly valuable areas must be protected from encroachment and other disturbance

## Slide 23: 15. A Good Built Environment
Cities, towns and other built-up areas must provide a good, healthy living environment and contribute to a good regional and global environment
Natural and cultural assets must be protected and developed
Buildings and amenities must be located and designed in accordance with sound environmental principles and in such a way as to promote sustainable management of land, water and other resources

## Slide 24: 16. A Rich Diversity of Plant and Animal Life
Biological diversity must be preserved and used sustainably for the benefit of present and future generations
Species habitats and ecosystems and their functions and processes must be safeguarded
Species must be able to survive in long-term viable populations with sufficient genetic variation
People must have access to a good natural and cultural environment rich in biological diversity, as a basis for health, quality of life and wellbeing

## Slide 25: Rationale of Environmental standards
Report issued by an expert group on the subject of environmental health should place great emphasis on criteria and standards.
Public health are dependent upon standardized values, procedures and substances

## Slide 26
Examples –
Motor Vehicle emission – authority for other sources of atmospheric pollution
Water supply under interstate carriers but not for water used in schools, offices, hospitals etc.,
Need for functional rather than categorical approach to standards developed
Move on set up of standards initiated by Public Health Service - effect from 1 Jan, 1967

## Slide 27
Authorities includes –
Public Health Service
Bureau of Disease Prevention and Environmental Control
Five national centers concerned - air pollution, radiological health, urban and industrial health, communicable disease control, and chronic disease control

## Slide 28
Statutory authority for developing criteria and enforcing standards for the following
Control of air pollution
Interstate spread of communicable disease
Ionizing radiations
Solid wastes
Accidental injuries, occupational hazards
Pesticides
Noise
Control of rodents, mosquitoes, and other
vectors of disease

## Slide 29
Extended study and consultation both within and outside the Public Health Service
Determined - any health protection standard promulgated by Bureau should meet the characteristics like-

## Slide 30: Characteristics
Standard should be truly relevant to the health and well-being of man
Should be addressed to the prevention or control of a health hazard or to other statutory responsibilities of the Public Health Service.

## Slide 31
Standard must be realistic and attainable
Standard should – employ the best available methods of control under conditions which are economically feasible and which do not constitute unacceptable risks to human health
Health protection standards should be attainable within the current state of the art and at a financial cost which is not prohibitive

## Slide 32
Adherence to the standard should be measurable with reasonable precision and reliability
Responsible for enforcing and also those who are required or expected to comply with the standard must be able to ascertain when a violation· has taken place

## Slide 33
Standard should be aggressive in terms of protecting the public health
Uncertainties as to the degree of control necessary should, be resolved in that direction which will afford the greater protection to the public

## Slide 34
Standard should clearly identify the population group it is intended to protect
Example: some standards are designed to protect the general population
- Some to protect a segment of the population
- Some to protect persons living in certain
geographic areas
- Some to protect workers in certain occupation
groups

## Slide 35: EFFLUENT AND STREAM STANDARDS
STREAM PROTECTION MEASURES
Methods of maintaining a stream
Effluent Standards
Stream Standards
Effluent Standard: The Quality Standards established for the wastewater that has been processed from the units.
Stream Standard: The Standard Quality established in accordance with the designation of water bodies

## Slide 36: EFFLUENT STANDARDS
Effluent standards pertain to the quality of the discharge water itself
Based on economics than on absolute protection of the stream
Easy to control
Detailed stream analysis are not required
It do not establish an overall level of pollutant loading for a given water body
Ratio of wastewater to stream flow are not considered
Treatment is obligatory irrespective of the size of industry

## Slide 37
For effective protection of an overloaded stream, the effluent standards are required to be upgraded
Large industries have an edge over small industry

## Slide 38: EFFLUENT DISPOSAL STANDARDS Table 1: Effluent disposal standards
Sl.No. | CHARACTERISTICS | STREAM CLASSIFICATION |  |  |  | 
 |  | A | B | C | D | E
1 | Dissolved Oxygen mg/L (Min) | 6 | 5 | 4 | 4 | -
2 | Biochemical Oxygen Demand mg/L (Max) | 2 | 3 | 3 | - | -
3 | Total Coliform Organism MPN/100mL | 50 | 500 | 5000 |  | 
4 | Total Dissolved Solids mg/L (Max) | 500 | - | 1500 | - | 2100
5 | Chlorides (as Cl.mg/L (Max.) | 250 | - | 600 | - | 600

## Slide 39: STREAM STANDARDS
Stream standards refer to the quality of the receiving water downstream from the origin of the wastewater discharge
It is based on establishing classification of quality for a stream
Quality of the receiving water is regulated to maintain established stream classification
Prevention of excessive pollution/ Loading is limited to what the stream can assimilate
No consideration of type and location of industry

## Slide 40
Allows public to establish goals for present and future water quality
Confusion of zone of different classification
Controversy over proportion of stream to be reserved for future usage (municipal, industrial, agriculture etc.)
Opposition from industry/ public to change the established classification

## Slide 41
A detailed stream analysis is required to determine the level of wastewater treatment required to maintain the health of the ecosystem
Cost of treatment may affect the survival of industry

## Slide 42: STREAM CLASSIFICATION IN INDIA Table 2: Stream classification
CLASS OF STREAM | DESIGNATED BEST USE
A | Drinking Water Source without conventional treatment after disinfection
B | Outdoor bathing
C | Drinking Water with conventional treatment followed by disinfection
D | Propagation of wild life-fisheries
E | Irrigation, industrial cooling controlled wastewater disposal

## Slide 43: Concentration and Mass
Concentration
Concentration is the mass of a pollutant in a defined volume of water
Load (Mass)
Load is the amount (mass) of a pollutant that is discharged into a water body during a period of time (i.e. tons of sediment per year)
Both concentration and load provide information of environmental significance, but each has limitations

## Slide 44: Minimum national standards (MINAS)
1976 – CPCB developed concept of evolving industry specific effluent standards
Based on comprehensive study of the problems of the industry
An attempt was made
To identify relevant pollution parameters
Its pollution potential
Best pollution control technologies available in India

## Slide 45: MINAS
MINAS contemplated a minimum level of treatment for specific industrial wastewater – based on
Annual turnover of the industry
Techno-economic feasibility of the control objective
Initially textile and man-made fibers were studied and standards were set
Later included oil refineries, chloro-alkali etc.,

## Slide 46
Disposal specificity was not a part of MINAS
Standards were considered to be minimum standards that a specific industry should achieve irrespective of the mode of disposal
In Environmental Protection Act 1986, some of these standards were incorporated
Since these were minimal standards – SPCB were permitted to make them only stringent and in no case relax them

## Slide 47: Two basic problems
Since these standards were not disposal specific , it lead to many anomalous situations
Tended to become rather stringent and in many cases almost the maximum achievable standards
MINAS are indeed not minimal standards but maximum achievable standards

## Slide 48: Emission and ambient standards
Ambient air quality refers to the condition or quality of air surrounding us in the outdoors
National Ambient Air Quality Standards are the standards for ambient air quality set by the Central Pollution Control Board (CPCB) that is applicable nationwide.
The CPCB has been conferred this power by the Air (Prevention and Control of Pollution) Act, 1981.

## Slide 49: Ambient Air Quality Standards in India
The Air (Prevention and Control of Pollution) Act 1981 was enacted by the Central Government with the objective of arresting the deterioration of air quality
The Air (Prevention and Control of Pollution) Act 1981 describes the main functions of the Central Pollution Control Board (CPCB) as follows

## Slide 50
To advise the Central Government on any matter concerning the improvement of the quality the air and the prevention, control and abatement of air pollution.
To plan and to be executed a nation-wide programme for the prevention, control and abatement of air pollution.
To provide technical assistance and guidance to the State Pollution Control Board

## Slide 51
To carry out and sponsor investigations and research related to prevention, control and abatement of air pollution
To collect, compile and publish technical and statistical data related to air pollution and
To lay down annul standards for the quality of air

## Slide 52: Table 1: National Ambient Air Quality Standards
Pollutant | Time Weighted Average | Concentration in Ambient Air | 
 |  | Industrial, Residential, Rural and Other Areas | Ecologically Sensitive Area (notified by Central Government)
Sulphur Dioxide (SO2), µg/m3 | Annual* 24 hours** | 50- 80 | 20 -80
Nitrogen Dioxide (NO2), µg/m3 | Annual* 24 hours** | 40- 80 | 30 -80
Particulate Matter (size less than 10 µm) or PM10 µg/m3 | Annual* 24 hours** | 60- 100 | 60 -100
Particulate Matter (size less than 2.5 µm) or PM2.5 µg/m3 | Annual* 24 hours** | 40- 60 | 40 -60
Ozone (O3) µg/m3 | 8 hours* 1 hour** | 100- 180 | 100 -180
Lead (Pb) µg/m3 | Annual* 24 hours** | 0.50 -1.0 | 0.50 -1.0

## Slide 53
Maximum amount of a specific pollutant allowed to be discharged into the atmosphere from a single fixed or mobile source.

## Slide 54
Environmental Performance Evaluation

## Slide 55: Environment Performance Indicators
Purpose
1. Environmental performance indicators provide
information that
Helps evaluation and
Decision making within organizations that engage in environmental efforts

## Slide 56
2. Environmental performance indicators provide a common foundation of information for
Organizations and external interested parties (such as consumers, business partners, residents in local communities, shareholders, and financial institutions) and
It helps interest parties’ proper understanding of activities of the organizations and their environmental efforts

## Slide 57
3. Environmental performance indicators provide a common foundation of information that helps the integration of environmental policies of the national and local governments, such as basic environment plans, and environmental activities of organizations

## Slide 58: Objective of EPI
1. To measure and evaluate environmental burdens, environmental problems that need to be solved and outcomes of environmental efforts comprehensively in order to promote environmental activities of organizations and to obtain information that helps decision making regarding these activities.

## Slide 59
2. To provide a common foundation of information between an organization and interested parties in order to facilitate that interested parties, such as consumers, business partners, residents in local communities, shareholders, and financial institutions, understand environmental activities of the organization

## Slide 60
3. To provide a common foundation of information for macro-level environmental policies of the national and local governments

## Slide 61: Table 2: Structure of Environmental Performance Indicators Operational Indicators
Core Indicators | Input | Total Energy Input Total Amount of Material Input Water Resource Input
 | Output | Amounts of Greenhouse Gases Emissions Amounts of Release and Transfer of Chemical Substances Total Amount of Production or Sales Total Amount of Waste Generation Total Amount of Final Disposal of Waste Total Amount of Water Drainage

## Slide 62
Sub Indicators | Indicators That Qualitatively Supplement the Core Indicators | Breakdown of Energy Input Kinds of Resources, State of the Resources at the time of input Breakdown of Water Resources Emissions of Substances Under the Kyoto Protocol Amounts of Emissions of Other Substances Under Regulations Amounts of Products or Services that Are Measured in Unit Other than Weight Amount of Production or Sales of Products that Contribute to Reduction of Environmental Burden

## Slide 63
 |  | Amount of Production or Sales of Products with Certified Environmental Labelling Amount of the Use of Containers and Wrappers Methods of Waste Disposal Kinds of Waste Generated Kinds of Water Area Where Wastewater are discharged Quality of Water

## Slide 64
 | Environmentally important indicators which may not be applicable to all business organizations - Indicators that would be important for establishing sustainable society | Repeated Use of Water within the Organization Emission of Sulfur Dioxide and Nitrogen Oxide Concentration in Emissions that are under Regulation Noise, Vibration, Odor Nitrogen, Phosphorus Concentration in Water Emissions that are under Regulation Repeated Use of Materials within the Organization Recycled Materials within the Organization Thermally Recycled Materials within the Organization

## Slide 65
 |  | Energy Efficiency for Each product Group Amount of CO2 Emission (From Use of Product) Proportions of Reusable and Recyclable Part for Each Product Group Amount of Products, Container and Wrappers Collected Amount of Consumed Material, Containers and Wrapper Reused, Recycled and Thermally Recycled, and its Proportion State of Contamination in Soil, Ground Water and Sediment Area of Greening, Planting Trees, and Restoration Amount of Chemical Substance Storage

## Slide 66: Environmental Management Indicators (Sub-Indicators)
Sub-Indicator | Environmental Management Systems Technology for Environmental Protection, Research and Development for Designing for the Environment of Products and Services Environmental Accounting Green procurement (purchase) Environmental Communication and Partnership Compliance with Environmental Law and Regulations Occupational Safety and Health Social Contribution concerning the environment

## Slide 67
Sub-Indicator | Management Indicators that Measure Efficiency with Combination With Operation Indicators | Amount of Sales Amount of production Area of Floor Number of Employees, Etc.
 | Indicators that Are Related to Management Indicators | Indicators that Measure Eco-efficiency Integrated Indicators of Environmental Burden

## Slide 68: Closing the loop
Production system in which the waste or by-product of one process or product is used in market for another product
Example : recycling waste newspaper to
make paper-board or other type of
paper

## Slide 69
Buying recycled products is part of Closing the Loop
Step is critical because it maintains the market demand for recyclables
Without a demand for recycled products, there is no economy to support recycling
Creating stable markets for recycling ensures the continuation and expansion of recycling programs everywhere

## Slide 70: pollution prevention
Pollution prevention is an environmental approach fundamentally different from approaches that focus on managing or controlling pollution after it has been generated
Pollution prevention occurs prior to the creation of a waste or a pollutant and thus occurs prior to the consideration of alternatives such as pollution control, waste management, treatment, recycling or disposal

## Slide 71: Barriers of pollution prevention
REGULATORY BARRIERS TO POLLUTION PREVENTION
End-of-Pipe Focus
In most instances, the end-of-pipe focus of existing regulations does not create a direct barrier to pollution prevention.
Potential negative effect of focusing industrial and public resources on controlling pollutants after it has been created rather than on product, process, or raw material changes

## Slide 72
b) Media-Specific Focus
Current regulations address one environmental medium at a time.
The result can be transfer of pollutants from one environmental medium to another and concentration on media-specific solutions rather than multi-media preventive approaches.
Media-specific focus does not always encourage multi-media preventive approaches

## Slide 73
c) Regulatory Program Evaluation Criteria
Current benchmarks for measuring the success of programs do not include consideration of pollution prevention progress
The focus is on more easily quantified performance measures such as the number of permits issued or the number of inspections performed.

## Slide 74
d) Regulatory Inflexibility
Lack of flexibility can sometimes create a barrier to pollution prevention
Pollution prevention is a customized process, varying facility by facility.
May require flexibility and short-term variances in compliance schedules for emission standards or permits

## Slide 75
e) Regulatory Uncertainty
Industry personnel working to implement pollution prevention strategies may be required to consult with several agencies and with decision-making authority.
Innovative project or a pollution prevention proposal may require multiple approvals for different aspects of that project, which may be difficult to obtain. This can discourage facilities from undertaking pollution prevention practices.

## Slide 76
f) Pollution Fees
If structured on a multi-media basis with a significant correlation to quantities of pollutants created and set at sufficient levels, fees can provide incentives for pollution prevention
Current fees are for the most part media-specific, set at levels determined by the costs of regulatory services, and in some cases are not closely correlated with quantities of pollutants released.
Although fees set up in this manner do not present direct barriers to pollution prevention, it provide little incentive to go beyond standards and prevent pollution at the source.

## Slide 77
g) Data Gathering and Management
Data gathering and management systems have generally developed along media-specific lines.
It focus on end-of-pipe emissions and quantities of waste generated as a means of enforcing and ensuring compliance with existing regulatory requirements.
Need for improved data relating to pollution prevention is recognized at both the federal and state levels.

## Slide 78
2. ECONOMIC BARRIERS TO POLLUTION
PREVENTION
Inaccurate Market Signals
In some instances, the costs of releasing toxic substances may be less than the cost of implementing a pollution prevention project
Because the full environmental cost of the release is not included in the calculation.

## Slide 79
b) Incomplete Cost/Benefit Analysis
Indirect benefits (e.g., lower future liabilities, potential for "environmental marketing" and positive investment image) are not commonly considered in an analysis and therefore do not reflect the advantages of implementing preventive projects.
Failure to take into consideration all relevant costs and benefits or failure to properly allocate these costs to appropriate operations and processes may present unnecessary barriers to pollution prevention.

## Slide 80
c) Inappropriately Short Time Horizons
Companies with very short-term perspectives on criteria for investment (e.g., 1-2 year payback periods) may be less likely to support certain prevention projects despite the fact that they would be economically viable in a moderate payback timeframe.

## Slide 81
d) Fear of Market Share Loss/Consumer Pressure
Surveys suggest that the most significant barrier to pollution prevention is reluctance to tamper with proven processes for fear of adverse effects on product quality

## Slide 82
e) Inappropriate Product/Process Specifications
Very specific cases involving the barrier, "fear of customer loss," result from unnecessarily rigid specifications for products or processes.

## Slide 83
f) Fear of Production Interruption
If prevention options require major operational changes, equipment alterations or process modifications, companies may resist implementation because of concern about not being able to produce the product at all or having higher reject rates through less reliable actions

## Slide 84
g) Limited Access to Necessary Resources
Prevention projects can face stiff competition for limited internal capital resources also presents a significant barrier to pollution prevention.
Access to external sources of capital to fund prevention projects may also be limited. The shortage of staff resources

## Slide 85
h) Worker Fear of Job Loss
If employees or labor groups look upon pollution prevention as a threat to their jobs, these concerns may pose a barrier to pollution prevention efforts
Experience shows that companies with pollution prevention programs are often strengthened economically, and produce higher quality products in a more efficient manner.

## Slide 86
3) EDUCATIONAL BARRIERS TO POLLUTION
PREVENTION
a) Lack of Top Level Support. It is common for educational leaders to simply exclude pollution prevention and environmental protection from institutional priorities
b) Insufficient Faculty Motivation and Training Barrier is caused, in part, by the difficulty in creating new courses, unavailability of teaching aids (e.g., case studies and research pressures.

## Slide 87
c) Insufficient Student Interest. Student demand for treatment of environmental issues has been small, possibly because they haven’t yet seen a connection between job success and environmental expertise.
d) Inflexible Curriculum Requirements. At most educational institutions the degree coursework is already crowded with requirements and continually faces new demands to add more credits and topics. In many instances, there is simply little or no room to add pollution prevention into the program.

## Slide 88
e) Lack of Instructional Materials.
Not sufficient existing material (e.g., casebooks, text books or videos) that is easily available to integrate into existing classes.

## Slide 89
INSTITUTIONAL BARRIERS TO POLLUTION PREVENTION
Three categories of institutional barriers are
a) Organizational: Reflect the ways in which companies manage human and material resources.
b) Technical: Address the development and use of technologies and operational practices.
c) Societal: Describe some ways in which society impacts pollution prevention efforts.

## Slide 90
Lack of Top Management Support.
Lack of Clear Communication of Priorities or Support.
Organizational Structures may Separate Environmental Decisions from Production Decisions.
Habit and Inertia may Inhibit Change.
Lack of Involvement of affected Workers.
Reward System does not Focus on Pollution Prevention.
Firms may lack the Technical Ability to Apply Preventive Methods and Technologies.

## Slide 91
Frequent Changes to Output, Product Design and Other Factors may make Implementation more Difficult.
Lack of Information about Sources of Waste and Releases, Alternative Strategies, and Resources.
Preventive Applications of Currently available.
Perception that Pollution Prevention addresses only Manufacturing Processes.
Lack of Consumer Environmental Awareness.

## Slide 92: USEFUL WEBLINKS
https://www.youtube.com/watch?v=oHbTgSqGo5c
https://www.youtube.com/watch?v=hLIqZMVygAg
https://www.youtube.com/watch?v=IZ3CIMnj498