## Slide 1: Structured Procedures
Shanthala G.M
Associate Professor
Module 4
Subject Name:Verilog HDL Subject Code:17EC53
K.S. SCHOOL OF ENGINEERING AND MANAGEMENT, BANGALORE - 560109
DEPARTMENT OF ELETRONICS AND COMMUNICATION ENGINEERING

## Slide 2: Structured Procedures
There are two structured procedure statements in Verilog:
1)always and
2)initial statements

## Slide 3
Example 7-1 initial Statement
module stimulus;
reg x,y, a,b, m;
initial
m = 1'b0; //single statement; does not need to be grouped
initial
begin
#5 a = 1'b1; //multiple statements; need to be grouped
#25 b = 1'b0;
end
initial
begin
#10 x = 1'b0;
#25 y = 1'b1;
end
initial
128
#50 $finish;
endmodule

## Slide 4: result
0 m = 1'b0;
5 a = 1'b1;
10 x = 1'b0;
30 b = 1'b0;
35 y = 1'b1;
50 $finish;

## Slide 5: Combined Port/Data Declaration and Initialization
module adder (sum, co, a, b, ci);
output reg [7:0] sum = 0; //Initialize 8 bit output sum
output reg co = 0; //Initialize 1 bit output co
input [7:0] a, b;
input ci;
--
--
endmodule

## Slide 6: Combined ANSI C Style Port Declaration and Initialization
ANSI C style port declaration can also be combined with an initialization.
Example -Combined ANSI C Port Declaration and Variable Initialization
module adder (output reg [7:0] sum = 0, //Initialize 8 bit output
output reg co = 0, //Initialize 1 bit output co
input [7:0] a, b,
input ci
);
--
--
endmodule

## Slide 7: always Statement
All behavioral statements inside an always statement constitute an always block. The
always statement starts at time 0 and executes the statements in the always block continuously in a looping fashion.
This statement is used to model a block of activity that is repeated continuously in a digital circuit. An example is a clock generator module that
toggles the clock signal every half cycle.

## Slide 8: Clock generation
module clock_gen (output reg clock);
initial
clock = 1'b0;
always
#10 clock = ~clock;
Initial
#1000 $finish;
endmodule

## Slide 9: Procedural Assignments
Procedural assignments update values of reg, integer, real, or time variables. The value
placed on a variable will remain unchanged
until another procedural assignment updates
the variable with a different value

## Slide 10
assignment ::= variable_lvalue = [ delay_or_event_control ] expression
The left-hand side of a procedural assignment <lvalue> can be one of the following:
• A reg, integer, real, or time register variable or a memory element
• A bit select of these variables (e.g., addr[0])
• A part select of these variables (e.g., addr[31:16])
• A concatenation of any of the above

## Slide 11: Two types of procedural assignment statements:.
Blocking and Nonblocking
Blocking assignment statements are executed in the order they are specified in a sequential block.
A blocking assignment will not block execution of statements that follow in a parallel block.
The = operator is used to specify blocking
assignments.

## Slide 12
reg x, y, z;
reg [15:0] reg_a, reg_b;
integer count;
initial
begin
x = 0; y = 1; z = 1; //Scalar assignments
count = 0; //Assignment to integer variables
reg_a = 16'b0; reg_b = reg_a; //initialize vectors
#15 reg_a[2] = 1'b1; //Bit select assignment with delay
#10 reg_b[15:13] = {x, y, z} //Assign result of concatenation to
// part select of a vector
count = count + 1; //Assignment to an integer (increment)
end

## Slide 13: Nonblocking Assignment
Example
reg x, y, z;
reg [15:0] reg_a, reg_b;
integer count;
initial
begin
x = 0; y = 1; z = 1; //Scalar assignments
count = 0; //Assignment to integer variables
reg_a = 16'b0; reg_b = reg_a; //Initialize vectors
reg_a[2] <= #15 1'b1; //Bit select assignment with delay
reg_b[15:13] <= #10 {x, y, z}; //Assign result of concatenation
count <= count + 1; //Assignment to an integer (increment)
end

## Slide 14
Nonblocking assignments allow scheduling of assignments without blocking execution of the statements that follow in a sequential block.
A <= operator is used to specify nonblocking assignments.
Note that this operator has the same symbol as a relational operator, less_than_equal_to. The operator <= is interpreted as a relational operator in an expression and as an assignment operator in the context of a nonblocking assignment.

## Slide 15
1. reg_a[2] = 0 is scheduled to execute after 15 units (i.e., time = 15)
2. reg_b[15:13] = {x, y, z} is scheduled to execute after 10 time units (i.e.,
time = 10)
3. count = count + 1 is scheduled to be executed without any delay (i.e., time = 0)

## Slide 16: Application of nonblocking assignments
always @(posedge clock)
begin
reg1 <= #1 in1;
reg2 <= @(negedge clock) in2 ^ in3;
reg3 <= #1 reg1; //The old value of reg1
end

## Slide 17
At each positive edge of clock, the following sequence takes place for the nonblocking assignments.
A read operation is performed on each right-hand-side variable, in1, in2, in3, and reg1, at the positive edge of clock.
The write operations to the left-hand-side variables are scheduled to be executed at the time specified by the intra-assignment delay in each assignment.
The write operations are executed at the scheduled time steps. The order in which the write operations are executed is not important because the internally stored right-hand-side expression values are used to assign to the left-hand-side values..

## Slide 18: Web Links
https://www.youtube.com/watch?v=FWE0-FOoE4s
  Video link from altera on verilog HDL basics
https://ocw.mit.edu/courses/electrical-engineering-and-computer-science/6-884-complex-digital-systems-spring-2005/lecture-notes/l02_verilog.pdf
  Power point presentation from MIT.
https://www.youtube.com/watch?v=PJGvZSlsLKs
  NPTEL Video from Prof Indranil Senguptha, IIT Kharagpur on Introduction to Hardware Modeling using verilog